## Slide 1
Lecture: Frequency domain analysis
Frequency response
Frequency response
Definition
The frequency response of a linear dynamical system with transfer function
G(s) is the complex function G(jω) of the real angular frequency ω ≥ 0
y(t)
G(s)
u(t) = U¯ sin(ωt)
Theorem
If G(s) is asymptotically stable (poles with negative real part), for
u(t) = U¯ sin(ωt) in steady-state conditions limt→∞ y(t) − yss(t) = 0, where
yss(t) = U¯ |G(jω)| sin(ωt + ∠G(jω))
The frequency response G(jω) of a system allows us to analyze the response of the system to sinusoidal excitations at different frequencies ω

## Slide 2: Frequency response – Proof
Lecture: Frequency domain analysis Frequency response
Set U¯ = 1 for simplicity. The input u(t) = sin ωt 1I(t) has Laplace transform
U(s) =
ω
s2 + ω2
yA(t) → 0 for t → ∞
As we are interested in the steady-state response, we can neglect the natural response yA(t) of the output. In fact, as G(s) is asymptotically stable,
The forced response of the output y(t) has Laplace transform
f
Y (s) = G(s)
=
ω G(s)ω
s2 + ω2 (s − jω)(s + jω)
Let’s compute the partial fraction decomposition of Yf (s)
ωG(jω) ωG(−jω)
s Yss (s) = steady˛-s¸tate response s
Yf (s) = 2jω(s − jω) + −2jω(s + jω) +
n
.
i=1
Ri
s − p
i
s ˛¸ s
transient forced response
1
1
i
R =residue of G(s
ω
s +ω
2 2
i
) in s = p . We are assuming here that G(s
) has distinct poles

## Slide 3: Frequency response – Proof (cont’d)
Lecture: Frequency domain analysis Frequency response
As G(s) is asymptotically stable, the inverse Laplace transform
B −1
Ri
i=1 s − pi
Σ Σ
n n
. .
i=1
= Riepit tends to zero asymptotically
The remaining steady-state output response is therefore
yss(t) = B
−1
2j(s − jω)
+
G(jω) G(−jω)
−2j(s + jω)
Σ Σ
−j
2
= G
jωt
j
2
(jω)e + G
(−jω)e
−jωt
−j
2
jωt
.
−j
2
= G(jω)e + G
(jω)e
jωt
Σ
Σ
−j
2
= 2ℜ G(j
jωt
Σ
ω)e =
Im Σ|G(jω)|ej∠G(jω)+jωt)Σ s ˛¸ s
2
Re(−j(a + jb)) = Re(−ja − j b) = Re(b − ja) = b
= |G(jω)| sin(ωt + ∠G(jω))
We can repeat the proof for U¯ /= 1 and get the general result.
Q

## Slide 4
Lecture: Frequency domain analysis
Frequency response
Example
y(t)
10
tt(s) =
(1 + 0.1s)2
u(t) = 5 sin 10t
The poles are p1 = p2 = −10, the system is asymptotically stable The steady-state response is
yss(t) = 5|G(jω)| sin(ωt + ∠G(jω))
where
=
10 10
(1 + 0.1jω)2 1 + 0.2jω − 0.01ω2
G(jω) =
For ω = 10 rad/s,
G(10j) =
10 5
1 + 2j − 1 j
= = −5j
Finally, we get
ss
y (t) = 5 · 5 sin
π
2
(10t − ) = 25 sin
π
2
(10t − )

## Slide 5
Lecture: Frequency domain analysis
Frequency response
Example (cont’d)
0
0.5
1.5
2
−30
−20
−10
30
20
10
0
1
time (s)
y (t)
ss
y(t)
u(t)
u(t) = 5 sin(10t)
ss
π
2
→ y (t) = 25 sin(10t − )

## Slide 6: Frequency response of discrete-time systems
Lecture: Frequency domain analysis Frequency response
y(k)
G(z)
u(k) = U¯ sin(kθ)
A similar result holds for discrete-time systems:
Theorem
If G(z) is asymptotically stable (poles inside the unit circle), for
¯
k→∞ ss
u(k) = U sin(kθ ) in steady-state conditions lim y(k) − y (k) = 0,
where
yss(k) = U¯ |G(ejθ )| sin(kθ + ∠G(ejθ ))

## Slide 7
Lecture: Frequency domain analysis
Bode plot
Bode plot
U¯ |tt(jω)| sin(ωt + ∠tt(jω))
U¯ sin(ωt)
tt(s)
The Bode plot is a graph of the module |G(jω)| and phase ∠G(jω) of a transfer function G(s), evaluated in s = jω
The Bode plot shows the system’s frequency response as a function of ω, for all ω > 0
Hendrik Wade Bode (1905–1982)

## Slide 8
Lecture: Frequency domain analysis
Bode plot
Bode plot
Bode phase plot
Bode magnitude plot −10
−20
−30
0
Magnitude (dB)
10
10
0
10
1
10
2
10
3
−270
−1
−225
−180
−135
−90
−45
−50
−60
−70
−80
0
Phase (deg)
Bode plot of G(s)
Frequency (rad/sec)
−40 G(s) =
1
(1 + 0.1s)(1 + 0.002s + 0.0001s
2 )
Example: frequency response of a telephone, approx. 300–3,400 Hz,
good enough for speech transmission
10
The frequency ω axis is in logarithmic scale
The module |G(jω)| is expressed as decibel (dB)
|G(jω)|db = 20 log10 |G(jω)|
Example: the DC-gain G(0) = 1, |G(j0)|db = 20 log 1 = 0
MATLAB
»bode(G)
»evalfr(G,w)

## Slide 9
Lecture: Frequency domain analysis
Bode
Bode form
To study the frequency response of the system is useful to rewrite the transfer function G(s) in Bode form
G(s) =
h
K Πi(1 + sτi)
j j
s Π (1 + sT )
i
2ζ
’
i
ω’ni
ω
’ 2
ni
Π 1 + s + s
1 2
. Σ
.
2ζ
j
ωnj
1
j ω2
nj
Π 1 + s + s
2
Σ
K is the Bode gain
h is the type of the system, that is the number of poles in s = 0
Tj (for real Tj > 0) is said a time constant of the system
ζj is a damping ratio of the system, −1 < ζj < 1
ωnj is a natural frequency of the system

## Slide 10
Lecture: Frequency domain analysis
Bode
Bode magnitude plot
10
.
|G(jω)|dB = 20 log .
.
h
K Πi(1 + jωτi)
i
.
’
i
2jζ ω
ω’
ni
Π 1 + −
ω
2
ω’ 2
ni
Σ
(jω) Πj(1 + jωTj) Π
j
.
2jζ ω
ωnj
1 + −
2
nj
.
Σ .
j ω .
ω2 .
Recall the following properties of logarithms:
α
β
log αβ = log α + log β , log = log α − log β ,
log αβ = β log α
Thus we get
|G(jω)|
dB
= 20 log10 |K| − h · 20 log10 ω
.
i
.
j
10 i 10 j
+ 20 log |1 + jωτ | − 20 log |1 + jωT |
.
i
10
+ 20 log 1 +
2jζ’i ω
. ω’
ni
−
ω
2
ω
’
ni
. .
2 .
.
j
10
.
.
− 20 log 1 +
2jζjω
ω
nj
−
2
ω
2
nj
ω .
.

## Slide 11
Lecture: Frequency domain analysis
Bode
Bode magnitude plot
We can restrict our attention to four basic components only:
|G(jω)|dB = 20 log10 |K| −h ·20 log10 ω
s ˛¸ s s ˛¸ s
#1 #2
i
10
+ 20 log |1 + j
i
. .
j
ωτ | − 20 log10 |1 + jωTj|
s #˛¸3 s
.
i
10
.
+ 20 log 1 +
2jζ’i ω
. ω’
ni
−
ω
ω
’
.
2 .
2 .
ni j
10
.
− 20 log 1 +
. j
2jζ ω
ω
nj
−
2
ω
2
nj
ω .
.
s
#˛¸4 s

## Slide 12
Lecture: Frequency domain analysis
Bode
Bode magnitude plot
Basic component #1
20 log10 |K|
1
jG(j!)jdb
20 log10jKj
10
100
1000 !
20
40
-20
Basic component #2
20 log10 |ω|
−20 log10 |ω|
jG(j!)jdb
1
10
100
1000 !
20
40
-20

## Slide 13
Lecture: Frequency domain analysis
Bode
Bode magnitude plot
Basic component #3
20 log10 |1 + jωT|
|G(j
ω)| ≈ 1 for ω
1
T
|G(j
ω)| ≈ ωT for ω
1
T
1
10
100
1000 !
20
jG(j!)jdb
40
-20
3
1
T
20
db/decade
0
Basic component #4
10
.
.
20 log 1 + 2jζ −
ω ω
2
2
ωn ωn
.
.
|G(j
ω)| ≈ 1 for ω ω
n
|G(j
ω2
ω
2
n
ω)| ≈ for ω ω
n
1
!
10
20
jG(j!)jdb
40
-20
40
db/decade
100 !n 1000
³ ¸ 0
³ crescente
6
0
³=
1
1
,
2
For ζ < the peak of the response is obtained
,
at the resonant frequency ωpeak = ωn 1 − 2ζ2

## Slide 14
Lecture: Frequency domain analysis
Bode
Example
G(s) = 1000(1 + 10s)
s2(1 + s)2
jG(j!)jdb
!
decade
-60 db/
0
50
100
Draw the Bode plot of the transfer function
150
40
-
db
/decade
-2
0 db
/decade
0.1
-50
0.01
1
10
100
For ω 0.1: |G(jω)| ≈
1000
ω2
ω2
For ω = 0.1: 20 log10 1000 = 20 log10 105 = 100
For 0.1 < ω < 1: effect of zero s = −0.1, increase by 20 dB/decade For ω > 1: effect of double pole s = −1, decrease by 40 dB/decade

## Slide 15
Lecture: Frequency domain analysis
Bode
Bode phase plot
∠G(j
ω) = ∠


h
K Πi(1 + jωτi)
j j
(jω) Π (1 + jωT )
i
.
’
i
2jζ ω
ω’ni
Π 1 + −
ω
ω
’
2
2
ni
.
2jζjω
nj
Πj 1 + ω −
ω
2
ω
2
nj
Σ
Σ 

Because of the following properties of exponentials
∠(ρejθ ) = θ
∠(αβ) = ∠(ραejθα ρβ ejθβ ) = ∠(ραρβ ej(θα +θβ )) = θα + θβ = ∠α + ∠β
β
α
α ρ e
jθ
α
β
ρ e
jθ
β
ρ
ρβ
∠ = ∠ = ∠ e
α β
α j(θ −θ )
. Σ
α β
= θ − θ = ∠α − ∠β
we get
∠G(jω) = ∠K − ∠ .(jω)hΣ
i
+ ∠(1 + j
. .
j
i j
ωτ ) − ∠(1 + jωT )
i
. .
+ ∠ 1 +
2jζ’i ω
ω’
ni
−
ω
ω
’
2
ni
Σ
2 .
j
.
− ∠ 1 +
2jζjω
ω
nj
−
ω
2
ω
2
nj
Σ

## Slide 16
Lecture: Frequency domain analysis
Bode
Bode phase plot
We can again restrict our attention to four basic components only:
s˛¸s
#1
∠G(jω) = ∠K − ∠ (jω)
h
. Σ
s ˛¸ s
#2
i
+ ∠(1 + j
i
. .
ωτ ) − ∠(1 + jωTj)
j s ˛¸ s
#3
i
. .
+ ∠ 1 +
2jζ’i ω ω’
ni
−
ω
ω
’
2
Σ
2 .
ni j
.
− ∠ 1 +
2jζjω ω
nj
−
ω
2
ω
2
nj
s
Σ
s
#˛¸4

## Slide 17
Lecture: Frequency domain analysis
Bode
Bode phase plot
Basic component #1
∠K =
.
0 for K > 0
−π for K < 0
1
10
100
1000 !
¼=2 \G(j!)
-¼=2
0
K>0
-¼ K<0
Basic component #2
h
. Σ
∠ (jω) =
hπ
2
1
10
100
1000 !
¼=2 \G(j!)
-¼=2
0 h=0
h=1
-¼ h=2

## Slide 18
Lecture: Frequency domain analysis
Bode
Bode phase plot
Basic component #3
∠(1 + jωT) = atan(ωT)
∠G(j
ω) ≈ 0 for ω
1
T
∠G(j
π
1
2 T
ω) ≈ for ω , T > 0
∠(1 − jωT) = −atan(ωT)
1
10
100
1000 !
¼=2 \G(j!)
-¼=2
0
¼=4
-¼=4
1
T
T>0
T<0
Basic component #4
ωn
∠ .1 + 2jζ −
ω ω
2
ω2
n
Σ
∠G(jω) ≈ 0 for ω ωn
2
π
For ζ ≥ 0, ∠G(jω) = for ω = ωn,
ω
2
2
ωn
. Σ
∠G(jω) ≈ ∠ − = π for ω ωn
1
10
¼=2
0
¼ \G(j!)
100 !n 1000 !
³ ¸ 0
³ crescente

## Slide 19
Lecture: Frequency domain analysis
Bode
Example (cont’d)
G(s) = 1000(1 + 10s)
s2(1 + s)2
jG(j!)jdb
!
0.1
0.01
1
10
100
-¼
-¼=2
-3¼=4
-5¼=4
-3¼=2
For ω 0.1: ∠G(jω) ≈ −π
For 0.1 < ω < 1: effect of zero in s = −0.1, add
π
2
π
2
Per ω > 1: effect of double pole in s = −1, subtract 2 = π

## Slide 20
Lecture: Frequency domain analysis
Bode
Example
G
10(1 + s)
(s) = s2(1 − 10s)(1 + 0.1s)
0
-4
Frequenza (rad/s)
Fase (deg)
Modulo (db)
-100
-50
0
50
100
10
10
-1
1
10
10 2
-200 -2
-100
-150
-50
0
60
-
40
-
0
-6
10
ω2
For ω 0.1: |G(jω)| ≈ (slope
=-40 dB
/dec), ∠G(jω) ≈ −π
ω2
For ω = 0.1: 20 log10 10 = 60 dB
For 0.1 < ω < 1: effect of unstable pole s = 0.1, decrease module by
20 dB/dec, increase phase by
π
2
π
2
For 1 < ω < 10: effect of zero s = −1, +20 dB/dec module, + phase
π
2
For ω > 10: effect of pole s = −10, -20 dB/dec module, - phase

## Slide 21
Lecture: Frequency domain analysis Bode
Summary table for drawing asymptotic Bode plots
 |  | magnitude | phase
stable real pole | T > 0 | −20 dB/dec | −π/2
unstable real pole | T < 0 | −20 dB/dec | π/2
stable real zero | τ > 0 | +20 dB/dec | π/2
unstable real zero | τ < 0 | +20 dB/dec | −π/2
pair of stable complex poles | ζ > 0 | −40 dB/dec | −π
pair of unstable complex poles | ζ < 0 | −40 dB/dec | π
pair of stable complex zeros | ζ’ > 0 | +40 dB/dec | π
pair of unstable complex zeros | ζ’ < 0 | +40 dB/dec | −π

## Slide 22: More on damped oscillatory modes
Lecture: Frequency domain analysis Bode
Let s = a ± jb be complex poles, b /= 0
Since (s − (a − jb))(s − (a + jb)) = (s − a)2 + b2 = s2 − 2as + (a2 + b2) =
a
a b
2 +b2 2 + 2
2 2 2a 1 2
(a + b )(1 − s + s ), we get
n
,
2 2
ω = a + b = |a ± jb|,
a
ζ = − ,
a2 + b2
= − cos ∠(a ± jb)
Note that ζ > 0 if and only if a < 0
n n
,
Vice versa, a = −ζω , and b = ω 1 − ζ
2
The natural response is
n
−ζω t
n
,
2
Me sin(ω 1 − ζ t + φ)
where M, φ depend on the initial conditions
The frequency ωd = ωn,1 − ζ2 is called damped natural frequency

## Slide 23: Zero/pole/gain form and Bode form
Lecture: Frequency domain analysis Bode
Sometimes the transfer function G(s) is given in zero/pole/gain form (ZPK)
G(s) =
’
h
i i
K Π (s − z )
i
i ni
Π s + 2ζ ω s + ω
2 ’ ’ ’
2
ni
. Σ
.
s Π (s − p ) 2
j j nj
j j Π s + 2ζ ω s + ω
2
nj
Σ
The relations between Bode form and ZPK form are
τi
1 1
Ti
zi = − , pj = − , K = K’
i i i
Π (−z )Π ω
’
2
ni
j j i
Π (−p )Π ω
2
ni
MATLAB
»zpk(G)

## Slide 24
Lecture: Frequency domain analysis
Nyquist plot
Nyquist (or polar) plot
Let G(s) be a transfer function of a linear time-invariant dynamical system The Nyquist plot (or polar plot) is the graph in polar coordinates of G(jω) for
ω ∈ [0, +∞) in the complex plane
G(jω) = ρ(ω)ejφ(ω), where ρ(ω) = |G(jω)| and φ(ω) = ∠G(jω)
The Nyquist plot is one of the classical methods used in stability analysis of linear systems
The Nyquist plot combines the Bode magnitude & phase plots in a single plot
Harry Nyquist (1889–1976)

## Slide 25
Lecture: Frequency domain analysis
Nyquist plot
Nyquist plot
−1
−0.8 −0.6 −0.4 −0.2
0.2
0.4
0.6 0.8 1
−0.8
−0.6
−0.4
−0.2
0
−20 dB
−10 dB
−6 dB
−4 dB
0 dB −2 dB
0.2
20 dB
0.4
10 dB
0.6 6 dB
0.8
4 dB 2 dB
To draw a Nyquist plot of a transfer function G(s), we can give some hints:
Nyquist plot of G(s)
0
Real Axis
Imaginary Axis
G(s) =
1
(1 + 0.1s)(1 + 0.002s + 0.0001s2 )
For ω = 0, the Nyquist plot equals the DC gain G(0)
If G(s) is strictly proper, limω→∞ G(jω) = 0
In this case the angle of arrival equals
(n − n
− + − + π +[
−]
z z p p 2 z[p]
− n + n ) , where n is the #
of zeros [poles] with positive [negative] real
part
G(−jω) = G(jω)
A system without any zero with positive real part is called minimum phase

## Slide 26: Nyquist criterion
Lecture: Frequency domain analysis Nyquist criterion
Consider a transfer function G(s) = N(s)/D(s) under unit static feedback
u(t) = −(y(t) − r(t))
As y(t) = G(s)(−y(t) + r(t)), the closed-loop transfer function from r(t) to y(t)
is
W(s) = G(s) = N(s)
1 + G(s) D(s) + N(s)
Nyquist stability criterion
The number NW of closed-loop unstable poles of W(s) is equal to the number NR of clock-wise rotations of the Nyquist plot around s = −1 + j0 plus the number NG of unstable poles of G(s). [NW = NR + NG]
Corollary: simplified Nyquist criterion
For open-loop asympt. stable systems G(s) (NG = 0), the closed-loop system W(s) is asymptotically stable if and only if the Nyquist plot G(jω) does not encircle clock-wise the critical point −1 + j0. [NW = NR]

## Slide 27
Lecture: Frequency domain analysis
Nyquist criterion
Nyquist stability criterion
Proof:
Follows by the Argument principle: “The polar diagram of 1 + G(s) has a number of clock-wise rotations around the origin equal to the number of zeros of 1 + G(s) (=roots of N(s) + G(s)) minus the number of poles of
1 + G(s) (=roots of D(s)) of 1 + G(s)”
The poles of W(s) are the zeros of 1 + G(s)
Q
Note: the number of counter-clockwise encirclements counts as a negative number of clockwise encirclements
Use of Nyquist criterion for open-loop stable systems:
draw the Nyquist plot of G(s)
count the number of clockwise rotations around −1 + j0
1
2
3
if −1 + j0 is not encircled, the closed-loop system W(s) = G(s)/(1 + G(s)) is stable
The Nyquist criterion is limited to SISO systems

## Slide 28
Lecture: Frequency domain analysis
Nyquist criterion
Example
=
10 10
(s + 1)2 s2 + 2s + 1
under static output
Consider the transfer function G(s) =
feedback u(t) = −(y(t) − r(t))
−2
0
2
6
8
10
−8
−6
−4
−2
0
2
8
6
4
Nyquist Diagram
4
Real Axis
Imaginary Axis
MATLAB
»G=tf(10,[1 2 1])
»nyquist(G)
The closed-loop transfer function is
W(s) = G(s)
1 + G(s)
The Nyquist plot of G(s) does not encircle
−1 + j0
By Nyquist criterion, W(s) is asymptotically stable

## Slide 29
Lecture: Frequency domain analysis
Nyquist criterion
10
s3 + 3s2 + 2s + 1
under unit output feedback
Example
Consider the transfer function G(s) = u(t) = −2(y(t) − r(t))
−10
−5
10
15
20
−25
−20
−15
−10
−5
25
20
15
10
5
0
Nyquist Diagram
0 5
Real Axis
Imaginary Axis
MATLAB
»G=tf(10,[1 3 2 1]); K=2
»nyquist(K*G)
»L=feedback(G,K)
»pole(L)
-3.8797
0.4398 + 2.2846i
0.4398 - 2.2846i
The closed-loop transfer function is
2G(s)
W(s) = 1 + 2G(s)
The Nyquist plot of 2G(s) encircles −1 + j0
twice
By Nyquist criterion, W(s) is unstable

## Slide 30: Dealing with imaginary poles
Lecture: Frequency domain analysis Nyquist criterion
Re(ω)
+
j0 x
no poles on imaginary axis
Re(ω)
0 x
+
pole(s) in s = 0 (counted as stable)
Re(ω)
0 x
+
jω0x
The Nyquist plot is generated by a closed curve, the Nyquist contour, rotating clock-wise from 0 − j∞ to 0 + j∞ and back to 0 − j∞ along a semi-circle of radius ∞, avoiding singularities of G(jω)
We distinguish three types of curves, depending on the number of poles on the imaginary axis:
Im(ω) Im(ω) Im(ω)
ω+
jω0 x −
ω+
0
ω0−
0
ω0−
pole(s) in s = ±jω
(counted as stable)

## Slide 31: Stability analysis of static output feedback
Lecture: Frequency domain analysis Nyquist criterion
Under static output feedback u(t) = −K(y(t) − r(t)), the closed-loop transfer function from r(t) to y(t) is
W(s) = KG(s)
1 + KG(s)
The number of encirclements of −1 + j0 of KG(s) is equal to the number of
1
K
encirclements of − + j0 of G
(s)
To analyze closed-loop stability for different values of K is enough to draw
1
K
Nyquist plot of G(s) and move the point − + j0 on the real axis
G(s) =
60
(s2 + 2s + 20)(s + 1)
I0=no unstable closed-loop poles I2 =two unstable closed-loop poles I1=an unstable closed-loop pole

## Slide 32: Phase margin
Lecture: Frequency domain analysis Phase and gain margins
Mp
Rtt(jω)
tt(jωc)
Assume G(s) is open-loop asymptotically stable
Let ωc be the gain crossover frequency, that is |G(jωc)| = 1
To avoid encircling the point −1 + j0, we want the phase ∠G(jωc) as far away as possible from −π
The phase margin is the quantity
Mp = ∠G(jωc) − (−π)
If Mp > 0, unit negative feedback control is asymptotically stabilizing For robustness of stability we would like a large positive phase margin
stt(jω)
1+ j0

## Slide 33: Gain margin
Lecture: Frequency domain analysis Phase and gain margins
Assume G(s) is open-loop asymptotically stable
Let ωπ be the phase crossover frequency such that ∠G(jωπ) = −π
To avoid encircling the point −1 + j0, we want the point G(jωπ) as far as possible away from −1 + j0.
The gain margin is the inverse of |G(jωπ)|, expressed in dB
Mg = 20 log10
1
|G(jωπ)|
= −|G(jω )|
π dB
1
Mg
Rtt(jω)
For robustness of stability we like to have a large gain margin
stt(jω)
1+ j0
tt(jωπ )
Sometimes the gain margin is defined as
g
M =
1
π
|G(jω )|
and therefore G
π
1
(jω ) = − Mg + j0

## Slide 34: Stability analysis using phase and gain margins
Lecture: Frequency domain analysis Phase and gain margins
G(s) =
8
s3 + 4s2 + 4s + 2
The phase and gain margins help assessing the degree of robustness of a closed-loop system against uncertainties in the magnitude and phase of the process model
They can be also applied to analyze the stability of dynamic output feedback laws u(t) = C(s)(y(t) − r(t)), by looking at the Bode plots of the loop function C(jω)G(jω) (see next lecture on “loop shaping”)

## Slide 35: Stability analysis using phase and gain margins
Lecture: Frequency domain analysis Phase and gain margins
However in some cases phase and gain margins are not good indicators, see the following example
stt(jω)
1+ j0
Rtt(jω)
Mp
The system is characterized by a large phase margin, but the polar plot is very close to the point (−1, 0)
The system is not very robust to model uncertainties changing G(s) from its nominal value
In conclusion, phase and gain margins give good indications on how the loop function should be modified, but the complete Bode and Nyquist plots must be checked to conclude about closed-loop stability