## Slide 1: Linear Control Systems

## Slide 2: Module 1: Lecture 1
Introduction to
Systems and Control

## Slide 3: What is a System?
A collection of physical, biological or abstract components which together
perform an intended objective
A system gives an output (also called response) for an input (also called excitation)
System can be a collection of multiple sub-systems
System
Output /
Response
Input /
Excitation
System (with 4 sub-systems)
Output / Response
Input /
Excitation
SS1
SS2
SS3
SS4
+

## Slide 4: Examples of System
Motor
Input – Electrical energy (voltage)
Output – Mechanical energy (Torque / Rotation)
Air conditioner
Input – Electrical energy (voltage)
Output – Heat energy (Changes the ambient temperature)
Human body infected with a virus
Input – Drug administration
Output – Drug distribution & effect on the body
Vehicle (car or bus)
Input – Acceleration or Deceleration
Output – Vehicle displacement

## Slide 5: Nomenclature
S.No. | Variable Name | Symbol | Description
1 | Time | 𝑡 | Time instant
2 | Input | 𝑢(𝑡) | Input signal given to the system at time 𝑡
3 | Output | 𝑦(𝑡) | Output signal of the system at time 𝑡
4 | Delay | 𝛿 | Time delay in a signal
5 | Disturbance | 𝑤(𝑡) | Disturbance affecting the system at time 𝑡
6 | Function | 𝑓 | A defined relation between a set of variables
Some of the basic symbols to be used in this course:

## Slide 6: Classification of Systems
Variety of classifications are possible based on system features and applications
Some of the important classifications include:
  Linear and non-linear systems
  Static and dynamic systems
  Time invariant and time variant systems
  Causal and non-causal systems

## Slide 7: Linear Vs Non-Linear Systems
E.g. Resistor : 𝐼 =
Linear systems
Output of the system varies
linearly with input
Satisfy homogeneity and
superposition
𝑉
𝑅
Non-linear systems
Output of the system does
not vary linearly with input
Do not satisfy homogeneity
and superposition
𝑉
E.g. Diode: 𝐼 = 𝐼0(𝑒 𝜏 − 1)
Module 1: Lecture 1
I
𝑉
𝑉
I
7

## Slide 8: Static Vs Dynamic Systems
Static systems
At any time, output of the system depends only on present input
Memory less systems
  𝑦 𝑡 = 𝑓(𝑢 𝑡 )
  E.g. Resistor:
𝐼(𝑡) = 𝑉(𝑡)
𝑅
Dynamic systems
Output of the system depends on present as well as past inputs
Presence of memory can be
observed
𝑦 𝑡 = 𝑓(𝑢 𝑡 , 𝑢 𝑡 − 1 ,
𝑢 𝑡 − 2 , … )
E.g. Inductor:
1
𝐼(𝑡) = 𝐿 𝑉(𝑡)𝑑𝑡
𝑡
0

## Slide 9: Time Invariant Vs Time Variant Systems
Time invariant systems
Output of the system is independent of the time at which the input is applied
𝑦 𝑡 = 𝑓 𝑢 𝑡 ⟹ 𝑦 𝑡 + 𝛿 =
𝑓(𝑢 𝑡 + 𝛿 )
E.g. An ideal resistor
𝐼 𝑡 =
𝑉 𝑡
𝑅
⟹ 𝐼 𝑡 + 𝛿
𝑉(𝑡 + 𝛿)
𝑅
Time variant systems
Output of the system varies dependent on the time at which input is applied
𝑦 𝑡 = 𝑓 𝑢 𝑡 ⇏ 𝑦 𝑡 + 𝛿 =
𝑓(𝑢 𝑡 + 𝛿 )
E.g. Aircraft: Mass (𝑀) of aircraft changes as fuel is consumed
Acceleration: 𝑎 𝑡
= 𝐹(𝑡)
𝑀(𝑡)

## Slide 10: Causal Vs Non-causal Systems
Causal systems
Output is only dependent on inputs already received (present or past)
Non-anticipatory system
•
•
𝑦 𝑡 = 𝑓(𝑥 𝑡 , 𝑥 𝑡 − 1 , . . )
E.g.
Thermostat based AC
Motor or generator
Non-causal systems
Output depends on future
inputs as well
System anticipates future inputs based on past
𝑦 𝑡 = 𝑓(𝑥 𝑡 , 𝑥 𝑡 + 1 , . . )
E.g.
  Weather forecasting system
  Missile guidance system

## Slide 11: What is a Control System?
A system or mechanism which directs the input to other systems and regulates their output
Control system alters the response of a plant or system as
desired
Controller
Control System
Plant or
System
To be controlled
Control Input
Output
Desired Reference

## Slide 12: Disturbance
Controller
Control System
Plant or System
To be controlled
Control Input
Output
Desired Reference
Unwanted signals which affect the output of the system
E.g. People entering and leaving an AC room disturbs room
temperature
Controller has to eliminate the effects of disturbance
Disturbance

## Slide 13: Feedback in Control
Controller
Control System
Plant or System
To be controlled
Control Input
Response / Output
Desired
Reference
Feedback
Feedback senses the plant output and gives a signal which can be compared to the reference
Controller action (control input) changes based on feedback
Feedback enables the control system in extracting the desired
performance from the plant even in presence of disturbance
Disturbance

## Slide 14: Examples of Control Systems
What is the process or plant?
What is the output?
What is the desired input?
What are the subsystems?
What is the actuator?
Actual temp
Temp
Setting knob
Air
Conditioned
Room
On
Off Switch
Module 1: Lecture 1
14

## Slide 15: Examples of Control Systems
Air conditioner maintaining desired temperature:
Plant
Control system
Reference
Control Input
Output
Disturbance
Feedback
Temperatur e Setting Knob
ON OFF
Switch
Air Conditioner
Room
Desired Temperature
Actual Temperature
: Room
: Air Conditioner
: Desired temperature
: Compressor ON/OFF
: Output temperature
: Factors affecting ambient temperature
: Measured temperature
People in the Room
15

## Slide 16: Examples of Control Systems
Human steering an automobile:
Plant
Control system
Reference
Control Input
Output
Disturbance
Feedback
: Vehicle or automobile
: Human control
: Desired destination
: Steering mechanism
: Actual position
: Traffic conditions
: Sensing (Human Senses)
Human Control
Vehicle / Automobile
Steering
Mechanism
Actual position
Desired
Destination
Sensing
Traffic conditions
16

## Slide 17: Overview
17
Summary : Lecture 1
System with examples
Classification of systems
Control system & examples
Feedback & its significance
Contents : Lecture 2
Model & its significance
Types of math models
Methods of modelling systems
Steps of modelling systems