## Slide 1
Module 2: Lecture 3
Transfer Function Modelling Block Diagram Representation

## Slide 2: Motivation
How to find the response of a system for an given input signal?
E.g.
𝐿
𝑉𝑖 (𝑡) 𝐶 𝑉0(𝑡)
𝐼(𝑡) 𝑅
Photos Courtes
y:
𝑖
𝑉 (𝑡) = 𝑅𝐼(𝑡) + 𝐿 𝑑𝐼
1
𝑑𝑡 + 𝐶 𝐼𝑑𝑡
1
𝑉0(𝑡) = 𝐶 𝐼𝑑𝑡
Module 2: Lecture 3
Find 𝑉0 𝑡 for a
given signal 𝑉𝑖(𝑡)
3

## Slide 3: Motivation
3
To find the time response, we need to solve ordinary differential
equations (integro-differential equations)
When model equations are transformed to 𝑠 − domain, they turn
out to be algebraic equations which are comparably easy to solve
The transformed model in 𝑠 − domain is called transfer function model
It is a model which is applicable for all kinds of input signals

## Slide 4: Transfer Function
For an LTI system, transfer function is the ratio of the Laplace transform of the output to the Laplace transform of the input with the initial conditions being zero
Mathematically, if 𝑈(𝑠) is the Laplace transform of the input function and 𝑌(𝑠) is the Laplace transform of the output, the transfer function 𝐺(𝑠) is given by:
𝐺 𝑠
= 𝑌 𝑠
𝑈 𝑠
4

## Slide 5: Transfer Function as Impulse Response
Impulse signal (𝛿 𝑡 ) is infinitesimally narrow
and infinitely tall yet integrating to one
It takes zero value everywhere except at 𝑡 = 0
∞
𝛿 𝑡 = 1
−∞
If input to the system is the unit impulse, then the output is called the impulse response i.e.,
𝑢 𝑡 = 𝛿 𝑡 ⟹ 𝑈 𝑆 = 1 ⟹ 𝐺 𝑠 = 𝑌(𝑠)
That means transfer function is the Laplace
transform of the impulse response of an LTI
system when the initial conditions are set to zero
Impulse function 𝛿(𝑡)
5

## Slide 6: Steps to Finding Transfer Function
6
Find the model equations of the given system
Identify the system input and output variables
Take the Laplace transform of the model equations, assuming zero initial conditions
Find the ratio of the Laplace transform of the output to the
Laplace transform of the input

## Slide 7: Transfer Function : Example 1
𝑉𝑖 (𝑡)
𝑉𝑜(𝑡)
𝑅
𝐿
𝐶
1. Model Equations:
𝑖
𝑉 (𝑡) = 𝑅𝐼(𝑡) + 𝐿 𝑑𝐼
1
𝑑𝑡 + 𝐶 𝐼𝑑𝑡
1
𝑉0(𝑡) = 𝐶 𝐼𝑑𝑡
Module 2: Lecture 3
𝐼(𝑡)
Photos Courtes
y:
8

## Slide 8: Transfer Function : Example 1
Input and Output Variables:
– Input: 𝑉𝑖 𝑡
– Output: 𝑉𝑜 𝑡
Laplace Transform: (assuming initial conditions to be zero)
𝑖
𝑠𝐶
𝑉 (𝑠) = 𝑅𝐼(𝑠) + 𝑠𝐿𝐼(𝑠) + 1 𝐼(𝑠)
0
𝑠𝐶
𝑉 (𝑠) = 1 𝐼(𝑠)
4. Transfer Function:
𝐺 𝑠
𝑉 𝑠
𝑉𝑖 𝑠
1 𝐼(𝑠)
1
𝑅 + 𝑠𝐿 + 1 𝐼(𝑠) 𝑅 + 𝑠𝐿 + 1
𝐶𝑠 𝐶𝑠
= 0 = 𝑠𝐶 = 𝑠𝐶 =
1
𝑠2𝐿𝐶 + 𝑠𝑅𝐶 + 1

## Slide 9: Transfer Function : Example 2
Find the transfer function of a system described by following
𝑑3𝑦 𝑑2𝑦 𝑑𝑦 𝑑𝑢
equation: 𝑑𝑡3 + 10 𝑑𝑡2 − 5 𝑑𝑡 + 𝑦 = 10 𝑑𝑡 + 𝑢 with zero initial
conditions
Laplace Transform:
𝑌 𝑠 𝑠3 + 10𝑠2 − 5𝑠 + 1 = 𝑈 𝑠
10𝑠 + 1
Transfer Function:
𝐺 𝑠
= 𝑌 𝑠
𝑈 𝑠
=
10𝑠 + 1
𝑠3 + 10𝑠2 − 5𝑠 + 1

## Slide 10: Properties of Transfer Function
Transfer function of a system is independent of the magnitude and nature of input
Using the transfer function, the response can be studied for various
inputs to understand the nature of the system
Transfer function does not provide any information concerning the physical structure of the system i.e., two different physical systems can have the same transfer function
E.g. MSD system : 𝐺 𝑠
= 𝑋 𝑠 = 1 = 1 (𝑀 = 𝐵 = 𝐾 = 1)
𝐹 𝑠 𝑀𝑠2+𝐵𝑠+𝐾 𝑠2+𝑠+1
Series RLC circuit : 𝐺 𝑠
= 𝑉0 𝑠
𝑉𝑖 𝑠
𝑠2𝐿𝐶+𝑠𝑅𝐶+1
1 1
𝑠2+𝑠+1
= = (𝑅 = 𝐿 = 𝐶 = 1)

## Slide 11: Transfer Function : General Form
General form of transfer function of a system:
𝐺 𝑠
𝑌 𝑠 𝑏0𝑠𝑚 + 𝑏1𝑆𝑚−1 + ⋯ + 𝑏𝑚−1𝑠 + 𝑏𝑚
= 𝑈 𝑠 = 𝑎0𝑠𝑛 + 𝑎1𝑠𝑛−1 + ⋯ + 𝑎𝑛−1𝑠 + 𝑎𝑛
= 𝐾′ 𝑠 − 𝑧1 𝑠 − 𝑧2 … 𝑠 − 𝑧𝑚
𝑠 − 𝑝1 𝑠 − 𝑝2 … 𝑠 − 𝑝𝑛
𝑛: Order of the system
𝐾: System gain or Gain factor – A proportional value that relates the magnitude of the input to that of the output signal at steady state
𝑧1, 𝑧2, … , 𝑧𝑚: Zeros of the system
𝑝1, 𝑝2, … , 𝑝𝑛: Poles of the system
𝑛 ≥ 𝑚 because the system becomes non-causal and is not physically realizable if 𝑛 < 𝑚

## Slide 12: Poles and Zeros
Poles:
  Roots of the denominator polynomial of the transfer function
  Values of 𝑠 at which the transfer function becomes unbounded
lim 𝐺 𝑠 = ∞
𝑠→𝑝𝑖
Zeros:
  Roots of the numerator polynomial of the transfer function
  Values of 𝑠 at which the transfer function vanishes
lim 𝐺 𝑠 = 0
𝑠→𝑧𝑖
Poles and zeros together with the system gain 𝐾 characterise the input- output system dynamics

## Slide 13: Gain, Poles and Zeros : Example
6𝑠+12
Find the system gain, poles and zeros of the system with following transfer
function: 𝑠3+3𝑠2+7𝑠+5
𝐺 𝑠 =
6𝑠+12
𝑠3+3𝑠2+7𝑠+5
System gain: 𝐾 = 12
5
Zeros: 𝑠 − 2 = 0 ⟹ 𝑠 = 2 ⇒ 𝑧1 = 2
Poles: 𝑠3 + 3𝑠2 + 7𝑠 + 5 = 0 ⟹ 𝑠 = −1, −1 + 2𝑗, −1 − 2𝑗
⟹ 𝑝1 = −1, 𝑝2 = −1 + 2𝑗, 𝑝3 = −1 − 2𝑗
Note: Poles and zeros are purely real or appear in complex conjugates
(𝑎 ∓ 𝑗𝑏) because all the coefficients of transfer function are real

## Slide 14: Block Diagram : Motivation
How to visualise a complex system wih many components?
How to understand the flow and transformation of signals
in a complex system?
How to find the transfer function of a complex system?
Block Diagram Representation

## Slide 15: Block Diagram of a System
It is a short hand pictorial representation of the system which
depicts
  Each functional component or sub-system and
  Flow of signals from one sub-system to another
Block diagram provides a simple representation of complex
systems
Block diagram
enables calculating the overall system
each
transfer
of the
function provided the transfer functions of
components or sub-systems are known

## Slide 16: Components of Block Diagram
Block diagrams have four components:
  Blocks: To represent the components or sub-systems
𝐺(𝑠)
𝐺(s) is the transfer function of sub-system
2. Arrows: To represent the direction of flow of signals
𝑈(𝑠) 𝑌(𝑠)

## Slide 17: Components of Block Diagram
3. Summing points: To represent the summation of two or more signals
𝑈1(𝑠) 𝑌 𝑠
= 𝑈1 𝑠 − 𝑈2(𝑠)
+
−
𝑈2(𝑠)
4. Take-off points: To represent the branching of a signal
𝑈(𝑠)
𝑈(𝑠)

## Slide 18: Block Diagram Example
Module 2: Lecture 3
𝑉𝑖 (𝑡)
𝑉𝑜(𝑡)
𝑅
𝐶
𝐼(𝑡)
1
1 + 𝑠𝑅𝐶
𝑉0(𝑠)
𝑉𝑖(𝑠)
Transfer Function:
𝐺 𝑠
= 𝑉0 𝑠
𝑉𝑖 𝑠
=
1
1 + 𝑠𝑅𝐶
Photos Courtes
y:
19

## Slide 19: Typical Block Diagram Forms
Cascaded Form / Series Form:
  Components or sub-systems of a system are connected in series each
having its own transfer function
  Overall transfer function is product of individual transfer functions
𝐺2(𝑠)
𝐺1(𝑠)
𝐺3(𝑠)
𝑈(𝑠)
𝑌(𝑠)
Transfer Function: 𝐺 𝑠
𝑌 𝑠
= 𝑈 𝑠
= 𝐺1 𝑠 𝐺2 𝑠 𝐺3(𝑠)

## Slide 20: Typical Block Diagram Forms
Parallel Form:
  Components or sub-systems of a system are connected in parallel
  Overall transfer function is sum of individual transfer functions
𝐺2(𝑠)
𝐺1(𝑠)
𝐺3(𝑠)
𝑈(𝑠)
𝑌(𝑠)
Transfer Function:
= 𝑌 𝑠
𝑈 𝑠
𝐺 𝑠 = 𝐺1 𝑠 + 𝐺2
3
𝑠 + 𝐺 (𝑠)
+
+ +

## Slide 21: Typical Block Diagram Forms
𝐻(𝑠)
𝐺(𝑠)
𝐸(𝑠)
𝑌(𝑠)
Feedback Form:
– One component is present in the feedback loop of another component
Transfer Function:
𝑌 𝑠 = 𝐺 𝑠 𝐸 𝑠
𝑌 𝑠 = 𝐺 𝑠 [𝑈 𝑠 − 𝑌 𝑠 𝐻 𝑠 ]
𝑌 𝑠 = 𝐺 𝑠 𝑈 𝑠 − 𝐺 𝑠 𝐻 𝑠 𝑌(𝑠)
𝑌 𝑠 1 + 𝐺 𝑠 𝐻 𝑠 = 𝐺 𝑠 𝑈 𝑠
=
𝑌 𝑠 𝐺 𝑠
𝑈 𝑠 1 + 𝐺 𝑠 𝐻(𝑠)
𝑈(𝑠)
−
+
Negative Feedback Loop
𝑌 𝑠 𝐻(𝑠)

## Slide 22: Loading Effect on Transfer Function
Assumption: While deriving transfer function, there is no loading
i.e., no power is drawn at the output of the system
This assumption must be satisfied even while deriving transfer functions for each component in a block diagram
If one component is acting as a load on another component:
  Transfer function of each component cannot be determined separately
  Transfer function of both components combined should be determined
  Both components are put in the same block in the block diagram
representation

## Slide 23: Loading Effect : Example
Model Equations in Laplace form:
𝑖 1
𝑉 𝑠 = 𝑅𝐼 𝑠 + 1
𝑠𝐶
𝐼
1 2
𝑠 − 𝐼 𝑠
1
0
𝑉 𝑠
2
= 𝑅𝐼 𝑠 + 1
𝑠𝐶
𝐼2 𝑠 − 𝐼1 𝑠
(2)
𝑠𝐶
0 2
𝑉 𝑠 = − 1 𝐼 𝑠
(3)
𝑉𝑖 (𝑡)
𝑉0(𝑡)
𝐶
𝐶
𝑅 𝑅
𝐼1
𝐼2
RC Circuits
in cascade
y:
Photos Courtes

## Slide 24: Loading Effect : Example
Transfer function is obtained by elimination 𝐼1 𝑠 and 𝐼2(𝑠) from Eqs.1, 2, 3
𝑉0 𝑠
𝑉𝑖 𝑠
=
1
𝑅2𝐶2𝑠2 + 3𝑅𝐶𝑠 + 1
𝑉𝑖 (𝑡)
𝑉0(𝑡)
𝐶
𝐶
𝑅 𝑅
𝐼1
𝐼2
y:
Photos Courtes

## Slide 25: Loading Effect : Example
Module 2: Lecture 3
Observe:
𝑉0 𝑠
𝑉𝑖 𝑠
=
≠
1 1
𝑅2𝐶2𝑠2 + 3𝑅𝐶𝑠 + 1 1 + 𝑅𝐶𝑠 1 + 𝑅𝐶𝑠
Overall transfer function is not equal to product of transfer functions
of two RC circuits in cascade
This is because the assumption of no loading fails when individual transfer functions are derived
Here, the second RC circuit draws energy from the first one and hence its individual transfer function is not valid when in cascade
1
1 + 3𝑅𝐶𝑠 + 𝑅2𝐶2𝑠2
𝑉𝑖(𝑠)
𝑉0(𝑠)
≠
1
1 + 𝑠𝑅𝐶
1
1 + 𝑠𝑅𝐶
𝑉𝑖(𝑠) 𝑉0(𝑠)
26

## Slide 26: Block Diagram to Transfer Function: Example
Module 2: Lecture 3
Photos Courtes
y:
𝐼
𝑎
𝑅𝑎
𝐿𝑎
𝐸𝑎
𝐿𝑓
𝐸
𝑓
𝐼𝑓
𝑇𝑀, 𝜃
Motor
𝐽, 𝐷
+
−
Armature controlled DC motor
𝐸𝑏
27

## Slide 27: Block Diagram to Transfer Function: Example
Variables and Constants in the model:
𝑅𝑎 = resistance of armature (Ω)
𝐿𝑎 = inductance of armature (𝐻)
𝐼𝑎 = armature current 𝐴
𝐼𝑓 = field current (𝐴)
𝐸𝑎 = voltage applied to armature (𝑉)
– 𝐸𝑏 = back emf (𝑉)
𝑇𝑀 = torque developed by motor (𝑁𝑚)
𝜃 = angular displace of motor shaft (𝑟𝑎𝑑)
𝐽 = moment of inertia of motor and load referred to motor shaft (𝑘𝑔 − 𝑚2)
𝐷 = friction coefficient of motor and load referred to motor shaft
𝑁𝑚
𝑟𝑎𝑑−𝑠
𝐾𝑇: Motor torque constant
𝐾𝑏: Back emf constant

## Slide 28: Block Diagram to Transfer Function: Example
𝐾𝑇
1
𝐿𝑎𝑠 + 𝑅𝑎
1
𝐽𝑠 + 𝐷
𝐸𝑎(𝑠)
𝐾𝑏
−
+
𝐼𝑎(𝑠)
𝑇𝑀(𝑠) 𝑠𝜃(𝑠)
1
𝑠
𝜃(𝑠)
𝐸𝑎(𝑠)
𝑇𝐹 = 𝜃 𝑠 =
𝐾𝑇
𝑅𝑠
𝐽𝑠2 + 𝑠 𝐷 + 𝐾𝑇 𝐾𝑏 𝑅𝑠

## Slide 29: Summary : Module 2
Review of Laplace and Inverse Laplace transforms
Transfer Function and its properties
Block diagram representation of systems
Loading effect on transfer functions

## Slide 30: Contents: Module 3
Simplifying block diagrams of complex systems and finding transfer function
Time domain analysis of control systems