## Slide 1: EMF equation of a DC generator

## Slide 2
Consider a DC generator with the following parameters, P = number of field poles Ø = flux produced per pole in Wb (weber) Z = total no. of armature conductors A = no. of parallel paths in armature N = rotational speed of armature in revolutions per min. (rpm)
Now, Average emf generated per conductor is given by
dΦ/dt (Volts) ... eq. 1
Flux cut by one conductor in one revolution = dΦ = PΦ Wb
Number of revolutions per second (speed in RPS) = N/60
Therefore, time for one revolution = dt = 60/N (Seconds)

## Slide 3
From eq. 1,
emf generated per conductor = dΦ/dt = PΦN/60 (Volts) …..(eq. 2)
Above equation-2 gives the emf generated in one conductor of the generator. The conductors are connected in series per parallel path, and the emf across the generator terminals is equal to the generated emf across any parallel path. Therefore, Eg = PΦNZ / 60A
For simplex lap winding, number of parallel paths is equal to the number of poles (i.e. A=P),
Therefore, for simplex lap wound dc generator, Eg = ΦNZ / 60