## Slide 2
INTRODUCTION KIRCHOFF’S LAW
KIRCHOFF’S VOLTAGE LAW ( KVL ) ANALYSIS CIRCUIT OF KVL
KIRCHOFF’S CURRENT LAW ( KCL ) ANALYSIS CIRCUIT OF KCL
QUIZ

## Slide 3: HISTORY OF KIRCHOFF’S LAW
INTRODUCTION
TYPES OF KIRCHOFF’S LAW

## Slide 4
described two laws that became central to electrical engineering in 1845
The laws were generalized from the work of Georg Ohm
It’s can also be derived from Maxwell’s equations, but were
developed prior to Maxwell’s work
Gustav Robert Kirchhoff
(German physicist)

## Slide 5: What?
A pair of laws stating general restrictions on the current and voltage in an electric circuit.
The first of these states that at any given instant the sum of the voltages around any closed path, or loop, in the network is zero.
The second states that at any junction of paths, or node, in a network the sum of the currents arriving at any instant is equal to the sum of the currents flowing away.
How?

## Slide 6
KVL
Kirchoff Voltage Law
KCL
Kirchoff Current Law

## Slide 7: INTRODUCTION KVL
MESH ANALYSIS
EXERCISE

## Slide 8
Kirchhoff's Voltage Law - KVL - is one of two fundamental laws in electrical engineering, the other being Kirchhoff's Current Law (KCL)
KVL is a fundamental law, as fundamental as Conservation of Energy in mechanics, for example, because KVL is really conservation of electrical energy
KVL and KCL are the starting point for analysis of any circuit
KCL and KVL always hold and are usually the most useful piece of
information you will have about a circuit after the circuit itself

## Slide 9
Kirchoff’s Voltage Law (KVL) states that the algebraic sum of the voltages across any set of branches in a closed loop is zero. i.e.;
 Vacrossbranches = 0

## Slide 10
Below is a single loop circuit. The KVL computation is expressed graphically in that voltages around a loop are summed up by traversing (figuratively walking around) the
loop.
+
-
+ Vr1 -
+ Vr2 -
+ Vr3 -
10V
R1
R2
R3
Part of Traversal
Resulting KVL Equation: Vr1+Vr2+Vr3-10=0
Assumed current direction

## Slide 11
The KVL equation is obtained by traversing a circuit loop in either direction and writing down unchanged the voltage of each element whose “+” terminal is entered first and writing down the negative of every element’s voltage where the minus sign is first met.
The loop must start and end at the same point. It does not matter where you
start on the loop.
Note that a current direction must have been assumed. The assumed current creates a voltage across each resistor and fixes the position of the “+” and “-” signs so that the passive sign con-vention is obeyed.
The assumed current direction and polarity of the voltage across each resistor must be in agreement with the passive sign convention for KVL analysis to work.
The voltages in the loop may be summed in either direction. It makes no difference except to change all the signs in the resulting equation. Mathematically speaking, its as if the KVL equation is multiplied by -1. See the illustration below.

## Slide 12
+
-
+ Vr1 -
+ Vr2 -
+ Vr3 -
10V
R1
R2
R3
Part of Traversal
Resulting KVL Equation: Vr1+Vr2+Vr3-10=0
+
-
+ Vr1 -
+ Vr2 -
+ Vr3 -
10V
R1
R2
R3
Part of Traversal
Resulting KVL Equation: -Vr1-Vr2-Vr3+10=0
For both summations, the assumed current direction was the same
Summation of voltage terms may be done in either direction

## Slide 13
For both cases shown, the direction of summation was the same
Assuming the current direction fixes the voltage references
+
-
+ Vr1 -
+ Vr2 -
+ Vr3 -
10V
R2
Resulting KVL Equation: Vr1+Vr2+Vr3-10=0
R1
Assumed current direction
R3
+
+ Vr1 -
+ Vr2 -
+ Vr3 -
10V
R2
Resulting KVL Equation: -Vr1-Vr2-Vr3-10=0
R1
Assumed current
- direction
R3

## Slide 14
Analysis using KVL to solve for the currents around each closed loop of the network and hence determine the currents through and voltages across each elements of the network
Mesh analysis procedure
STEP 1
Assign a distinct current to each closed loop of the network
STEP 2
Apply KVL around each
closed loop of the network
STEP 3
Solve the resulting simultaneous linear equation for the loop currents

## Slide 15
Exercise 1
Find the current flow through each resistor using mesh analysis for the circuit below

## Slide 16
EXERCISE 1
SOLUTION
Assign a distinct current to each closed loop of the network
STEP 1
STEP 2
Apply KVL around each closed loop of the network
Solve the resulting simultaneous linear equation for the loop currents
STEP 3

## Slide 17
S
E
T
P 1

## Slide 18
Loop1:
I1R1I1R3 I2 R3  V1
10I1  40I1  40I2  10
50I1  40I2  10    equation1
Loop2 :
I2 R2  I2 R3 I1R3  V2
20I2  40I2  40I1  20
40I1  60I2  20    equation2
S
E
T
P 2

## Slide 19
DET1013 : ELECTRICAL TECHNOLOGY
40 20
10  1000  400  600
 50
20 60
40 60
40  3000 1600  1400
  50
20
40I 1   10
40 60I 
2
FromKCL :
I3  I1  I2  0.143A  0.429 A  0.286 A
 1400
I  I2  600  0.429 A
1
  0.143A
 1400
I  200
1
I 
2
I
1
40  600  800  200
I  10
  2   
50I1  40I2  10
40I1  60I2  20
Matrixform :
50
Solve equation 1 and equation 2 using Matrix
S
E
T
P 3

## Slide 20: INTRODUCTION KCL
NODES ANALYSIS
EXERCISE

## Slide 21: 1
Kirchhoff’s Current Law is sometimes called “Kirchhoff’s First Law” or
“Kirchhoff’s Junction Rule”
along with Kirchhoff’s Voltage Law makes up the two fundamental laws of Electrical Engineering
In this lesson it will be shown how Kirchhoff’s Current Law describes the current flow through a junction of a circuit
2

## Slide 22: 3
KCL helps to solve unknowns when working with electrical circuits
KCL with the addition of KVL and Ohm’s Law will allow for the solution of complex circuits
4

## Slide 23
Definition that will help in understanding Kirchhoff’s Current Law:
Examples of a Junction

## Slide 24
Kirchhoff’s Current Law generally states:
Restated as:

## Slide 25
The algebraic sum of all currents entering (+) and leaving (-) any point (junction) in a circuit must equal zero.
Here, the 3 currents entering the node, I1, I2, I3 are all positive in value and the 2 currents leaving the node, I4 and I5 are negative in value. Then this means we can also rewrite the equation as;
𝐼1 + 𝐼2 + 𝐼3 − 𝐼4 − 𝐼5 = 0

## Slide 26
Analysis using KCL to solve for voltages at each common node of the network and hence determine the currents though and voltages across each elements of the network.

## Slide 27
Determine the number of common nodes and reference node within the network
Common node
Assign current and its direction to each distinct branch of the nodes in the network
Current Direction
Apply KCL at each of the common nodes in the network
KCL
Solve the resulting simultaneous linear equation for the node voltage
Solve Equation
Determine I and V
Determine the currents through and voltages across each elements in the network

## Slide 28
Example 1:
Find the current flow through each resistor using node analysis for the circuit below.

## Slide 29: EXERCISE
Determine the number of common nodes and reference node within the network.
1 common node (Va)
and 1 reference node C
Assign current and its direction to each distinct branch of the nodes in the network (refer o the figure)
Apply KCL at each of the common nodes in the network
KCL: I1 + I2 = I3
REMEMBER THE STEPS EARLIER??

## Slide 30: (10- Va) + (20- Va) = Va 10 20 40
40
Va = 11.428V
Va ( 1 + 1 + 1 ) = 2
40 10 20
Va ( 7 ) = 2
1- Va +1- Va = Va
10 20 40
Va + Va + Va = 2
40 10 20
I3 = 11.428 = 0.286V 40
= 0.429A
20
10
(20-11.428)
I2 =
= - 0.143A
(10 -11.428)
I1 =

## Slide 31
Example 2:
Find the current flow through each resistor using node analysis for
the circuit below.

## Slide 32
Determine the number of common nodes and reference node within the network.
1 common node (Va)
and 1 reference node C
Assign current and its direction to each distinct branch of the nodes in the network (refer o the figure)
Apply KCL at each of the common nodes in the network
KCL: I1 = I2 + I3
REMEMBER THE STEPS EARLIER??

## Slide 33: (40- Va) = (Va - (-55))+ Va
5k 3k 6k 3k 5k
- Va ( 1 + 1 + 1 = 55 - 40
5k 3k 6k 3k 5k
- Va (700 x 10-6 ) = 10.33 x 10-3 Va = -14.757V
5k 3k 6k 40 - Va = Va + 55 + Va
6k 6k 3k 3k 6k (-Va) - Va - Va = 55 - 40
= - 2.46mA
6k
3k (-14.757)
I3 =
= 13.41mA
5k
(-14.757+ 55)
I1 =
I2 =
= 10.95mA
(40- (-14.757))

## Slide 34
Q1
Q2
Q3
Q4
Q5
Q6
Q7
Q8
Q9
Q10

## Slide 35: Kirchhoff’s First Law says that:
Current loses strength as it flows about a circuit
Voltage loses strength as it flows about a circuit
Wires need insulation to stop electrons from leaking out
of the wire
Total current flowing into a point is the same as the current flowing out of that point

## Slide 36: KCL is used when solving circuits with…
Closed loops
Sufficient nodes/ junctions
Capacitors
None

## Slide 37
Nodal Analysis applies the following principles…
KVL & Ohm’s Law
KCL & Ohm’s Law
KVL & Superposition
KCL & Superposition

## Slide 38: Which of the following statements is true?
Mesh Analysis employs KVL to solve loop currents
All of t All of the above
Mesh Analysis is easiest when a circuit has more than two nodes
Mesh Analysis is more difficult than Nodal Analysis

## Slide 39: Three
If a circuit contains three loops, how many independent equations can be obtained with Kirchhoff’s Second laws?
Four
Five
Six

## Slide 40
How much is current I3 in the node shown?
2A
-2A
0A
8A

## Slide 41
How much is current I4 in the node shown?
2A
-2A
18A
8A

## Slide 42
How much is voltage V3 in the closed loop circuit
shown?
2A
-2A
10A
-10A

## Slide 43
How much is voltage V4 in the closed loop circuit shown?
4A
-4A
8A
-8A

## Slide 44
Using KVL, find the value of Rx in the circuit shown
8Ω
4Ω
2Ω
1Ω

## Slide 45: Q1
Q2
Q3
Q4
Q6
Q5
Q7
Q8
Q10
Q9

## Slide 46: Q1
Q2
Q3
Q4
Q6
Q5
Q7
Q8
Q10
Q9