## Slide 1
SINUSOIDAL STEADY STATE ANALYSIS

## Slide 2: OBJECTIVES OF THIS PRESENTATION
Learning how to represent a sine function with phase
Learning about a phasor
Converting rectangular form to polar form and vice versa
Phase relationship for R,L,C and RLC circuits
Impedance
Phasor diagrams
A sample problem

## Slide 3: QUESTION???
How will you represent mathematically a sine / cosine wave function with phase???

## Slide 4: PHASOR
A sinusoidal current or voltage at a given frequency is characterized by only two
parameters
1. amplitude
2. phase angle
The complex representation of voltage is also characterized by the same two parameters.

## Slide 5: Assumed sinusoidal form
I=Imcos(wt+Φ)
I=jImcos(wt+Φ)=Imej(wt+Φ)
Complex form of the corresponding current

## Slide 6
Throughout any linear circuit , operating in a sinusoidal steady state at a given frequency w, every current or voltage may be characterized completely by the knowledge of its amplitude and phase angle.
None of the circuits we are considering will respond at a frequency other than that of the
excitation source, so that the value of ‘w’ is always known.
The complex representation of every voltage will contain the same factor ejwt. Hence, we can avoid carrying the redundant information throughout the solution.

## Slide 7
Hence,
•
I=ImejΦ
The complex quantities are usually written in polar form than exponential form to achieve a slight addition of time saving and effort.
Consider,
v(t)=Vmcoswt
It represented as VmL 0°
i(t)=Imcos(wt+Φ)
The real part of a complex quantity is i(t) = Re{Imej(wt+Φ)}
I=ImL Φ
This abbreviated representation is called a phasor

## Slide 8
Step 1
Step 2
Step 3
Step 4
i(t) = Imcos(wt+Φ)
i(t) = Re{Imej(wt+Φ)}
I=ImejΦ
I=ImL Φ

## Slide 9
Important Points to keep in mind:
1. In Phasor representation, phasors are complex quantities and hence are printed in boldface
type.
2. Capital letters are used for the phasor representation of an electrical quantity because the
phasor is not an instantaneous function of time; it contains only amplitude and phase angle

## Slide 10: PHASOR RELATIONSHIP FOR R,L AND C
Resistor
A
a.c. Source
R
V
Vmax
imax
Voltage
Current
Voltage and current are in phase, and Ohm’s law applies for effective currents and voltages.

## Slide 11
Inductor
A
L
V
a.c.
Vmax
imax
Voltage
Current
The voltage peaks 900 before the current peaks. One builds as the other falls and vice versa.

## Slide 12
Capacitor
Vmax
imax
Voltage
Current
A
V
a.c.
C
The voltage peaks 900 after the current peaks. One builds as the other falls and vice versa.

## Slide 13
Resistor
  V=I*R
Inductor
  V=jwL*I
Capacitor
  I=jwC*V
wL is called the inductive reactance (XL)
1/wC is called the capacitive reactance(XC)

## Slide 14: IMPEDANCE
Consider a Series R,L,C circuit
VL
VT
a.c.
L
Series ac circuit
A
R C
VR VC
Consider an inductor L, a capacitor C, and a resistor R all connected in series with an ac source. The instantaneous current and voltages can be measured with meters.

## Slide 15: Phasor Diagram
VR
VC
VL

VR
V - V
L C
VT
Source voltage

## Slide 16: V  V 2  (V V )2 R L C
T
tan  V L VC
VR
T
L
C
V  i R2  (X
 X )2

## Slide 17

R
XL - XC
Z
Impedance
T
L
C
V  i R2  (X  X )2
Z  R2 ( X  X )2
L C
T
V  iZ
or i  VT Z
The impedance is the combined opposition to ac current consisting of both resistance and reactance.

## Slide 18: PHASOR DIAGRAMS
1. The phasor diagram is a name given to a sketch in the complex plane showing
relationships of the phasor voltages and phasor currents throughout a specific circuit.
2. It also provides a graphical method for solving certain problems which may be used to check more exact analytical methods.
3.A phasor voltage 1cm long might represent 100V while a phasor current 1cm long might represent 3mA. Plotting both the phasors on the same diagram enables us to determine which waveform is leading or lagging.

## Slide 19
4. The phasor diagram also offers an interesting interpretation of the time-domain to
frequency-domain transformation.
5. In summary, the frequency-domain phasor appears on the phasor diagram and the transformation to the time domain is accomplished by allowing the phasor to rotate in a counter clockwise direction at a angular velocity of ‘w’ rad/s and then visualising the projection on the real axis

## Slide 20
Example:
V=6+j8=10L 53.1°
j8
6
53.1°
10

## Slide 21
THANK YOU