## Slide 1: SINGLE PHASE AC CIRCUITS ANALYSIS

## Slide 2: CONTENTS
1. AC CIRCUIT
  PURELY RESISTIVE CICUIT
  PURELY INDUCTIVE CIRCUIT
  PURELY CAPACITIVE CIRCUIT
AC SERIES CIRCUITS
  SERIES R-L CIRCUIT
  SERIES R-C CIRCUIT
  SERIES R-L-C CIRCUIT

## Slide 3: CONTENTS
•
•
•
•
2. RESONANCE
  RESONANCE IN SERIES
  RESONANCE IN PARALLEL
  RESONANCE FREQUENCY
VARIATION OF DIFF. QUANTITIES WITH
FREQUENCY
  INDUCTIVE REACTANCE
  CAPACITIVE REACTANCE
  CURRENT

## Slide 4: Introduction
AC CIRCUIT:
Circuits in which currents and voltages vary sinusoidally i,e vary with time are called alternating current or a.c circuits. All a.c circuits are made up of combination of resistance R , inductance L and capacitance C. The circuit elements R,L and C are called circuit parameters . To study a general a.c circuit it is necessary to consider the effect of each seperately.

## Slide 5: 1.1 Purely Resistive Circuits
Figure shows a circuit containing only resistance R
v = Vm sin ωt
By Ohm’s law, the instantaneous current in the circuit will be
i =v/R =Vm sinωt / R
Vm^/ R = Im
i=Im sinωt
Comparison of voltage equation and current shows that the phase difference are in phase difference between voltage and current is zero . Hence , in a circuit with resistance only the voltage and current are in phase with each other .

## Slide 6
The waveform and phase diagram respectively of the voltage and current in a circuit containing only a resistance .
Since maximum value = √2 * r.m.s. Value
Im = √2 I: Vm = √2 V
√2 V/R = √2 I V = RI
Above eq=n represents ohm’s law
It is noted that applied voltage is counter balanced by the voltage drop across the resistance R . This voltage drop is called resistive voltage drop and denoted by Vr .
Vr = V Vr = IR

## Slide 7: 1.2 Purely Inductive Circuit
Consider a purely inductive circuit containing only an inductance L
. Let the current taken by the circuit be
I = Imsinωt
This current produces a self induced e.m.f. eL in the circuit given by
eL= -L di/dt
At any instant two voltages are present in the circuit , one is the applied voltage eL . By KVL
v = - eL = L di/dt = L d(Imsin ωt)/dt
= ωLImcosωt = ωLImsin(ωt+ 900)
If ωLIm = Vm
v = Vm sin(ωt+ 900)
Comparison shows that the phase difference between voltage and current is 90 .

## Slide 8
If Φ is measured from the current phase Φ =
+900 .
Hence , in a purely inductive circuit the voltage leads the current by 900 or the current lags by 900.
The waveform and phasor diagram respectively of the voltage and current containing only on inductance .

## Slide 9: Inductive Reactance
ωL( I I) = V
ωL = V/I
The quantity ωL is the ratio of the r.m.s. voltage to r.m.s. current in purely inductive circuit . It is called the inductive reactance of the circuit and is denoted by the symbol XL . Since it is the ratio of voltage and current it is measured in ohms .
The opposition of inductance to the flow of alternating current is defined as the inductive reatance XL .

## Slide 10
Also ,
XL = ωL
= 2 πfL V = XL I
The voltage drop across the inductance L is called the inductive voltage drop . It is denoted by VL .
VL = V VL = XL I

## Slide 11: 1.3 Purely Capacitive circuit
Consider a purely capacitive circuit containing only a capacitor C connected to an a.c. Supply voltage given by
v= Vmsin ωt
The current in the circuit at any instant is
i =dq/dt
•
•
i =d (Cv)/dt = C dv/dt = C d(Vm
= ωCVm cos ωt = ωCVm
sinωt)/dt
sin(ωt+900)
ωCV ^ = I
m m
•
•
i = Im sin(ωt+900)

## Slide 12
Comparison shows that the phase difference Φ between the voltage and the current is 900. if Φ is measured from the voltage phasor Φ =
+900.Hence in purely capacitive circuit current
leads the voltage by 900.The waveforms and phasor diagram respectively for a circuit containing capacitance alone.

## Slide 13: Capacitive Reactance
•
•
ωC( √2V)= √2I
V/I=1/ωC
The ratio of r.m.s. Voltage to r.m.s. Current in a purely capacitive circuit is called the capacitive reactance. It is defined as the opposition offered by a purely capacitive circuit to the flow of sinusoidal current. The capacitive reactance is denoted by Xc and
•
•
is measured in ohms.
Xc= 1/ωC= 1/2πfC
V/I= X
V= XcI
The part of the supply which charges the capacitor is known as the capacititve voltage drop.
Vc= V
Vc= XcI

## Slide 14: 1.4 Series R-L Circuit
Consider a circuit containing a resistance R and an inductance L in series
Let V = supply voltage
I = circuit current
VR = voltage drop across R = RI
VL = voltage drop across L = XLI= 2πfLI
ΦL = phase angle between I and V
Since I is common to both elements R and L,this is used as reference phasor. The voltage VR is in phase with I and VL leads by 900 . The voltage V is the phasor sum of VR and VL that is the phasor diagram:

## Slide 15
The triangle having VR,VL and V as its sides is called voltage triangle for a series R-L circuit:
The phase angle ΦL between the supply voltage V and the circuit current I is the angle between the hypotenuse and the side VR .It is seen that
the current I is lagging behind the voltage V in an R-L circuit.
V2 = V2R + V2L
= (RI)2 + (XL I)2 V2/I2 = R2 + X2L
V/I = √(R2 + X2L)
•
•
•
•
•
•
•
ZL = √(R2 + X2L)
ZL is called the impedance of a series R-l circuit ZL = V/I
V = ZL I

## Slide 16: Impedance Triangle for a Series R- L Circuit
If the length of each side of the voltage triangle is divided by current I , the impedance triangle is obtained . The impedance triangle for a series R-L circuit is given. The following results may be found from an impedance triangle for a series R-L circuit:
•
•
•
•
ZL = √(R2 + X2L)
R = ZLcosΦL XL = ZL sinΦL
tanΦL = XL /R

## Slide 17: 1.5 Series R-C
Circuit
A circuit containing a resistance R and a capacitance C in series
Let V = supply voltage
I = circuit current
VR = voltage drop across R = RI
VC = voltage drop across C =XCI = I/2πfC
ΦC = phase angle between I and V
The voltage VR is in phase with I and VC lags I by 900 .The voltage sum is:
V = VR + VC

## Slide 18: The phasor diagram:
The triangle having VR , Vc and V as its side is called voltage triangle for
a series R-C circuit.
The phase angle ΦC between the supply voltage and the circuit current is the angle between the hypotenuse and the side VR . It is observed :
V2 = V2R + V2c
= (RI)2 + (Xc I)2 V2/I2 = R2 + X2c V/I = √(R2 + X2c)
Zc = √(R2 + X2c)
Zc is called the impedance of a series R-C circuit
Zc = V/I
V = Zc I

## Slide 19: Impedance Triangle for a Series R-
C Circuit
If the length of each side of the voltage triangle is divided by current I , the impedance triangle is obtained . The impedance triangle for a series R-C circuit is given. The following results may be found from an impedance triangle for a series R-C circuit:
ZC = √(R2 + X2 )
C
R = ZCcosΦC
XC = ZC sinΦC tanΦC = XC /R

## Slide 20: 1.6 Series RLC circuit
A circuit having R, l and C in series is called a general series circuit current is used as reference phasor in series circuit since it is common to all the elements of circuit. There are four voltages
VR in phase with I VL leading I by 900 VC lagging I by 900
Total voltage V = VR + VL + VC

## Slide 21: Phasor diagram:
VL and VC are in opp. Directions and their resultant is their arithmetic differnce
There are 3 possible cases in series RLC circuit
a. VL | > VC | i.e; Xl | > XC
b. VL | < VC | i.e; Xl | < XC
c. VL | = VC | i.e; Xl | = XC

## Slide 22
When XL > XC the circuit is predominantly inductive .
# Inductive circuits cause the current ‘lag’ the voltage.
•
•
V=I √[R2 + ( Xl - XC )2] Z = √[R2 + ( Xl - XC )2]
When XL < XC the circuit is predominately capacitive.
# Capacitive circuits cause the current to ‘lead’ the voltage.
•
•
V=I √[R2 + ( Xc - Xl )2] Z = √[R2 + ( Xc - XL )2]

## Slide 23: Impedance Triangle for RLC circuit
If the length of each side of a voltage triangle is divided by current I, the impedance triangle is obtained. The impedence triangle for series RLC circuit :

## Slide 24: 2. RESONANCE
Resonance is a condition in an RLC circuit in which the capacitive and inductive reactance are equal in magnitude, thereby resulting in a purely resistive impedance.
At resonance, the impedance consists only resistive component R.
The value of current will be maximum since the total impedance is minimum.
The voltage and current are in phase.
Maximum power occurs at resonance since the power factor is unity
Resonance circuits are useful for constructing filters and used in many application.

## Slide 25: 2.1 Series Resonance Circuit

## Slide 26: 2.2 Resonance in series RLC circuit
Total
Vs Vm
Im  Z  R
The impedance now
reduce to
ZTotal  R
Total impedance of series RLC
Circuit is
ZTotal  R  jX L - jX C
ZTotal  R  j(XL - XC )
At resonance
XL  XC
The current at resonance

## Slide 27: 2.3 Parallel Resonance

## Slide 28: At resonance, currents IL and IC are equal and cancelling giving a net reactive current equal to zero. Then at resonance the above equation becomes.

## Slide 29: We remember that the total current flowing in a parallel RLC circuit is equal to the vector sum of the individual branch currents and for a given frequency is calculated as:

## Slide 30: 2.4 Resonance Frequency
Resonance frequency is the frequency where the condition of resonance occur.
Also known as center frequency. Resonance frequency
rad/s
LC
1
o
ω 
1
fo  Hz
2 LC

## Slide 31: VARIATION OF DIFFERENT QUANTITIES WITH FREQUENCY

## Slide 32: 2.5 Variation of inductive
reactance with frequency
The inductive reactance XL =2∏fL is directly proportional to the frequency f .Hence its graph is a straight line through the origin

## Slide 33: 2.6 Variation of capacitive reactance with frequency
The capacitive reactance XC =1/2πfC is inversely proportional to the frequency . Hence its graph is a rectangular hyperbola XL versus f and XC versus f curves cut at a point where f=f0

## Slide 34: 2.7 Variation of current with frequency
The current versus frequency is known as resonance curve or response curve . The current has a maximum value at resonance given by I0 = V/R. The value of I decreases on either sides of the resonance

## Slide 35: THANK YOU